## Slide 1: Decentralizing a single-site test to lower Liquid Biopsy adoption hurdles
Dr. Verena Schramm
VP Application Product Management

## Slide 2: Cautionary notice
The information included in this presentation has been prepared for and is intended for viewing by a global audience. This presentation contains information about products which may or may not be available in different countries and if applicable, may or may not have received approval or market clearance by a governmental regulatory body for different indications for use. Please consult local sales representatives.
All product and company names are trademarks or registered® trademarks of their respective holders. Use of them
does not imply any affiliation with or endorsement by them.
SOPHiA GENETICS products are for Research Use Only and not for use in diagnostic procedures unless specified otherwise.

## Slide 3: Our Mission
Expand access to data-driven medicine by using AI
to deliver world-class care to patients across the globe.
A patient’s data in Boston today can help better diagnose and treat a patient with a similar profile in Madrid tomorrow

## Slide 4: Decentralizing MSK-ACCESS®
MSK-ACCESS® v1 (Analysis of Circulating cfDNA to
Evaluate Somatic Status)
Centralized test at MSK1–3
Targeted tumor-sequencing test for 129 genes
associated with rare and common cancers
NY state verification and validation of SNV and Indels; CNVs, fusions, MSI considered investigational
Matched blood sample analysis to distinguish somatic from germline & CHIP variants
Decentralized version of MSK-ACCESS® v2 with
146 genes curated by MSK experts
Research Use Only: Detects SNVs, Indels, CNVs, fusionsa
Matched blood sample analysis and proprietary molecular barcoding technology, CUMIN
MSK-ACCESS® powered with SOPHiA DDMTM
Decentralized application on the SOPHiA DDMTM Platform
aSNVs (P1), Indels (P1), CNVs (P2), and fusions (P2). MSI status detection is considered investigational and not available at the first commercial launch . P1 = verified variants; P2 = detectable variants pending concordance study. CHIP, clonal hematopoiesis of indeterminate potential; CNV, copy number variations; Indels, insertions and deletions; MSI, microsatellite instability; SNV, single nucleotide variants.
1. MSK. MSK-ACCESS®. Available at: https://www.mskcc.org/departments/division-solid-tumor-oncology/early-drug-development-service-phase-clinical-trials/precision-medicineapproach/msk-access; 2. Brannon AR, et al. Nature
Communications. 2021;12(1):3770. 3. In the News (11 June 2019). MSK-ACCESS Receives New York State Approval for New Molecular Assay. Available at: https://www.mskcc.org/news/msk-access-receives-new-york-state-approval-new-molecular-assay

## Slide 5: Overcoming challenges in cfDNA analyses
SOPHiA GENETICS approach
Limited input material
Efficient chemistry maximizes number of input molecules represented in final NGS library
Low ctDNA content (down to 0.5%) makes variants hard to detect
Variant calling algorithms (PEPPER ) based on CUMIN molecular identifiers
False positive variant calls when operating at low variant fractions
Molecular barcode technology, CUMIN enables efficient noise suppression
Challenges
Assay optimized for
20 ng cfDNA input
High sensitivity ≥ 0.5%
variant allele fraction (VAF)
High specificity
(99.99%)
Biological confounders (CH, germline) obscuring somatic variant identification
Inclusion of matched WBC DNA into data generation and bioinformatic workflow
Data on file.
© SOPHiA GENETICS 2024 | Confidential - For research use only - Not for use in diagnostic procedures
Evaluation of variants
for somatic support
cfDNA, cell-free DNA; CH, clonal hematopoiesis; ctDNA, circulating tumor DNA; WBC white blood cell.
Goal

## Slide 6: End-to-end concordance between MSK and SOPHiA GENETICS
Capture
ACCESS_v2
ACCESS_v1
1st/2nd/3rd level analysis
SG
pipeline
MSK
pipeline
Library Prep
SG
KAPA
SG
results
Variant calls
clinical cfDNA and matched WBC gDNA
samples
MSK
results
cfDNA, cell-free DNA; SG, SOPHiA GENETICS; WBC white blood cell.
© SOPHiA GENETICS 2024 | Confidential - For research use only - Not for use in diagnostic procedures
Klemm et al,
AMP 2024
Verification cohort (n=48) representative of routine clinical cases (at MSK)

## Slide 7: High analytical concordance with centralized MSK- ACCESS®
Annotation | ≥ 0.5% VAF
FN | 0
Flagged TP | 1
TP | 158
Extra Variants (FPs) | 30
% PPA | 99.4%
FN, false negative; FP, false positive; g, genomic; Indel, insertions and deletions; PPA, positive percent agreement; SG, SOPHiA GENETICS; SNV, single nucleotide variant; TP, true positive;
VAF, variant allele fraction; WBC, white blood cell.
99.4% positive percent agreement = sensitivity for SNVs/INDELs calling
0.5% variant allele frequency (VAF) limit of detection in clinical materials while maintaining high sensitivity
Analytical specificity of 99.999%
(0.0133 FP / kbp)
Klemm et al,
Capture
ACCESS_v2
ACCESS_v1
1st/2nd/3rd level analysis
SG pipeline
MSK pipeline
Library Prep
SG
KAPA
SG results
Variant calls
48 clinical cfDNA and matched WBC gDNA samples
MSK results
Comparison of SG performance to MSK results
AMP 2024
MSK VF (%)
7
R2=0.97
SOPHiA GENETICS VF (%)

## Slide 8: Streamlined end-to-end Liquid Biopsy workflow
cfDNA, cell-free DNA; CNVs, copy number variations; Indels, insertions and deletions; SNVs, single nucleotide variants; ULP, Universal Library Prep; WBC, white blood cell.

## Slide 9: SOPHiA DDM
MaxCare Program
Assessment
Adoption
Consulting
Sampling Strategy
Training
Fully guided set-up bringing routine analysis in-house
The SOPHiA DDM MaxCare Programs enables customers to rapidly
adopt a genomic application in their daily workflow by providing:
Consultation on off-the shelf and custom application options
Quality control material
Proficiency reports for each application
550+
MaxCare Programs from April 2018 to June 2024

## Slide 10: Overview of MSK ACCESS MaxCare sites
Site | Site | Progress | Sequencer | run | cfDNA material* |  | WBC | Confirmed Variants Provided | BCT | cfDNA extraction | Issues | Root cause
1 | USA North America | completed | NovaSeq 6000 | 1 | other, | SOPHiA ref materials | No | No | Roche | MagMax |  | protocol deviation: capture
1 |  | completed |  | 2 | other, | SOPHiA ref materials | No | No |  |  |  | 
2 | Germany Europe | completed | NovaSeq 6000 | 1 | clinical, contrived | SOPHiA ref materials | Yes | Yes, LDT | PAXGene Streck | Qiagen magn. beads |  | 
2 |  | completed |  | 2 | clinical, contrived | SOPHiA ref materials | Yes | No, LDT |  |  |  | 
3 | France Europe | completed | NextSeq 2000 | 1 | clinical, | SOPHiA ref materials | Yes | Yes, FMI | Roche | Qiagen silica membr. |  | 
3 |  | completed |  | 2 | clinical, | SOPHiA ref materials | Yes | Yes, FMI |  |  |  | 
4 | Canada North America | completed | NextSeq 2000 | 1 | clinical, | SOPHiA ref materials | No | Yes, LDT | Streck | MagMax |  | 
4 |  | completed |  | 2 | clinical, | SOPHiA ref materials | No | Yes, LDT |  |  |  | 
5 | Norway Europe | 1st run compl. | NovaSeq 6000 | 1 | contrived, | SOPHiA ref materials | No | No | not appl. | not. appl. |  | 
6 | UK Europe | completed | NovaSeq 6000 | 1 | clinical, | SOPHiA ref materials | Yes | Yes | PaxGene | MagMax Qiagen magn. beads |  | protocol deviation: clin. cfDNA low input
6 |  | completed |  | 2 | clinical, | SOPHiA ref materials | Yes | Yes |  |  |  | 
7 | USA North America | completed | NovaSeq 6000 | 1 | clinical, | SOPHiA ref materials | Yes | Yes | PaxGene | Maxwell |  | protocol deviation: clin. cfDNA low input
7 |  | completed |  | 2 | clinical, | SOPHiA ref materials | Yes | Yes |  |  |  | 
8 | Brazil South America | completed | NovaSeq 6000 | 1 | clinical, | SOPHiA ref materials | Yes | Yes | Streck | Qiagen silica membr. |  | 
8 |  | completed |  | 2 | clinical, | SOPHiA ref materials | Yes | Yes |  |  |  | 
9 | India Asia | 1st run compl. | NovaSeq 6000 | 1A | clinical, | SOPHiA ref materials | Yes | Yes | PaxGene | Qiagen silica membr. |  | 
9 |  | 2nd capt. pend. |  | 1B | clinical, | SOPHiA ref materials | Yes | Yes |  |  |  | protocol deviation: failed capture 2
Diverse set of blood collection tubes and cfDNA extraction reagents
All sites met QC targets (excluding IFU deviations)
Blue – non-AZ sponsored sites Pink – AZ-sponsored sites
10
contrived = externally sourced commercial cfDNA reference materials

## Slide 11: High inter-laboratory reproducibility
Site 5
Site 6
SeraCare 2.5% observed VAF
Site 1 Site 2 Site 3 Site 4
Replicates
Repeatability (intra-lab) |  |  |  |  | Reproducibility (inter-lab) | 
Expected VAF | Mean VAF | Expected SD* | SD | %CV | SD | %CV
2.5% | 2.34 | 0.23 | 0.34 | 14.5 | 0.35 | 14.8
0.5% | 0.48 | 0.10 | 0.14 | 29.6 | 0.15 | 30.1
At the assay LoD, site-to-site variance is equivalent to that observed within sites
This demonstrates the high robustness and consistency of the protocol and data analysis
Repeatability Reproducibility
SeraCare 0.5% observed VAF
Repeatability Reproducibility
Site 7
Site 1 2 Site 3 4 5
Replicates
6 7
11
*Expected SD based on a coverage of 5000x; SD = standard deviation; CV = coefficient of variance; LoD = limit of detection
Data on File.

## Slide 12: High concordance with single-site tests
12
Data on File.
© SOPHiA GENETICS 2024 | Confidential - For research use only - Not for use in diagnostic procedures
PPA = Positive Percent Agreement; TP = true positive; ETP = equivocal true positive (detected but filtered); FN = false negative; EP = extra
positive (extra variants); GM = germline mutation; CHIP = clonal haematopoiesis of indeterminate potential
Site | Samples | VAF cutoff | PPA | TP | ETP | FN | EP | GM ¦ CHIP | Confirmed variants
Site 2 | 7 | none | 100 | 6 | 0 | 0 | 36 | 2 | 8
 |  | ≥ 0.5% | 100 | 6 | 0 | 0 | 19 | 2 | 8
Site 3 | 22 | none | 86.6 | 79 | 15 | 3 | 114 | 37 | 134
 |  | ≥ 0.5% | 97.5 | 55 | 2 | 0 | 56 | 22 | 79
Site 4 | 19 | none | 94.1 | 16 | 1 | 0 | 81 | T-only | 17
 |  | ≥ 0.5% | 94.1 | 16 | 1 | 0 | 50 | T-only | 17
Site 7 | 16 | none | 86.2 | 40 | 5 | 4 | 76 | 16 | 65
 |  | ≥ 0.5% | 94.1 | 37 | 3 | 0 | 46 | 11 | 51
grey interval = 95% CI based on 2400x median molecule coverage
Observed vs reported VAF within the margin of stochastic molecule sampling
114/120 (95%) reported variants ≥
0.5% VAF detected
Note: duplicate samples were removed from analysis; PPA is calculated as (TP + CHIP) / Confirmed variants
Site 2 Site 3 Site 4 Site 7

## Slide 13: Global deployment demonstrates successful solution transfer
Experience from global community and our internal lab helps others to efficiently adopt liquid biopsy workflows
Community insights used to improve algorithms for challenging variant detection
Applying our wet-lab and bioinformatics expertise ensures high inter-laboratory reproducibility and high concordance with single site tests
Limit of detection optimized by combining expertise in
wet-lab workflows and biophysical theory
Biological “false positives” (clonal haematopoiesis of indeterminate potential) identifed via tumour-normal approach
High accuracy
Robust decentralized performance
Successful adoption
14.8% VAF CV between sites. 95.0% PPA with orthogonal tests.
LOD 0.5% VAF, detection down to
~0.1% VAF.
50/224 orthogonally reported variants of likely germline or CHIP origin.
Successful adoption in first sites.
Homopolymer variant calling improvements made.
14

## Slide 14: Partnership beyond MSK ACCESS powered with SOPHiA DDM
MSK-IMPACT® & MSK-ACCESS®
powered with SOPHiA DDM
s
14